## Slide 1: Dynamic Hardware Matrix Acceleration Design Reflection
Designed/Presented by David Cain
Special thanks to Omar Eddash and Adam Frost for mentorship

## Slide 2: Design Objective
Develop an FPGA based reconfigurable design to accelerate matrix convolution
This is a computationally intensive step used in many image processing algorithms
  can benefit from hardware acceleration
The design must accept multiple data types
  Integer data values
  Floating point data values
  Fixed point data values
Each of these data types can be dynamically reconfigured on device

## Slide 3: Intro to Vivado
Vivado is the primary software suite used when working with Xilinx based FPGAs such as the Pynq-Z2
Vivado offers design development using HDL or the built in IP Integrator using block diagrams
  These block diagrams can compose of either base IPs provided by Xilinx or user custom IPs that are imported/created within the project
  The HDL defining these Xilinx based IPs are not viewable by end-user
Often both development forms are used when working on a design

## Slide 4: Intro to Vivado (cont.)
Example of block diagram interface
  *For synthesis, block diagrams must be packaged with HDL wrappers generated by Vivado

## Slide 5: Learn Verilog
Upon entering the project, I was referenced this book and several tutorials to get a feeling of Verilog
  Free Range VHDL, Bryan Mealy, 2018
Xilinx also has tutorials with pre-built designs to be imported and demonstrate concepts of how to use the hardware available
YouTube tutorials were also helpful for workflow within Vivado

## Slide 6: Learn Verilog (cont.)
With a simple understanding of Verilog, basic designs were created and tested:
  Multibit flipflop register (FlipFlop.v)
  Parallel multibit flipflop (ParallelBuffer.v)
  Multibit port MUX (mux.v)
  Variable data slicer (dataSplit.v)

## Slide 7: Partial Reconfig Multipliers
A first step was to implement devices that could intake 2 data values, multiply them, then return the product
  This needed to be designed for three separate data types, with separate algorithms to complete each computation type
This was initially designed to buffer input data internally, allowing for parallel computations. The buffered input was removed due to adding undesirable delay while pipelining data streams

## Slide 8: Partial Reconfig Multipliers (cont.)
Block diagram of multiplier v1

## Slide 9: Partial Reconfig Multipliers (cont.)
Block diagram of multiplier v2

## Slide 10: Enabling Partial Reconfig
Using Vivado’s partial reconfiguration wizard, designs can become dynamically reconfigurable
This allows for partitions of the FPGA to be reprogrammed during runtime
When converting a project to partially reconfigurable, simulation is no longer available
  It is recommended to flesh out much of a PR design while static, then create a new project for a dynamic version
Notes: Mention how Vivado makes the whole project PR
When a project is PR, can’t to simulation
A static and dynamic version of the project was created

## Slide 11: Enabling Partial Reconfig (cont.)
Backup project
Enable Partial Reconfiguration
  Tools->Enable Partial Reconfiguration…
Select a device in top to create a partition definition
Notes: Mention how Vivado makes the whole project PR
When a project is PR, can’t to simulation
A static and dynamic version of the project was created

## Slide 12: Enabling Partial Reconfig (cont.)
Add any needed partitions and modules
Create a configuration with modules set as needed
Notes: Mention how Vivado makes the whole project PR
When a project is PR, can’t to simulation
A static and dynamic version of the project was created

## Slide 13: Enabling Partial Reconfig (cont.)
Each reconfigurable partition requires a dedicated pBlock to dictate the hardware available for reconfiguration
This pBlock should contain only the dynamic module. Static modules will be placed and routed automatically
This is a screenshot of the floorplan for a design with 8 pBlocks to enable 8 separate reconfigurable multiply compute partitions.
pBlock Definitions
Static Hardware

## Slide 14: Crossbar Data Switch
A data link was needed to interface many parallel multiplier outputs to many parallel adder devices
A crossbar switch was designed and implemented. This switch allows for any input port to be selected and connected to any output port.
  The crossbar was written from scratch to have variable input and output port counts
  These ports are also variable bit length
The data connection is asynchronous, mimicking wire connections

## Slide 15: Crossbar Data Switch (cont.)
The crossbar operates on a grid connection method. With N inputs and M outputs, this generates NxM valid address selections
At positive edge clocks, the address on AddressSelect port is toggled
If direct is HIGH, equal I/O ports will be connected.
  i.e. Output0 = Input0; Input1 = Output1;…
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16 Addresses
N = 4
M = 4

## Slide 16: Crossbar Data Switch (cont.)
Block diagram of crossbar

## Slide 17: Partial Reconfig Adder
With a method to now compute many products in parallel and sort them, a device was needed to accumulate the sum of products
2 Partition definitions were created:
  Integer/Fixed Point Adder
  Floating Point Adder
Floating point needs much more logic due to needing to check the magnitude difference, then normalize the values

## Slide 18: Matrix Accelerator
The devices were then packaged into a single IP, matrixAcclerator
  This device has a lot of I/O and no control logic
  It must be packaged with a controller IP
Hierarchy View
Block Diagram
Dynamic Partitions

## Slide 19: Asynchronous FIFO
The matrix accelerator needs much data input
  Data Set (Image Values)
  Filter Set (Filter Values)
Since the program will not be able to load values and operate the FPGA properly, an asynchronous FIFO buffer was used to input a data set across the clock domains

## Slide 20: Asynchronous FIFO (cont.)
There was a helpful online project:
  Crossing Clock Domains with an Asynchronous FIFO, Dan Gisselquist, 2018
  https://zipcpu.com/blog/2018/07/06/afifo.html
I attempted to write this IP from scratch, but the problem was difficult
This write-up by Gisselquist was an extensive overview of the device problems, behavior, and similar work

## Slide 21: Asynchronous FIFO (cont.)
To verify this FIFO design was suitable, it was first tested in Vivado simulation
Next, a bitstream and block diagram was generated to program the FPGA with the Python3 interface
In the Python environment, the buffer would be filled with a random data set
Next, the buffer data would be extracted and compared with original input
The load/compare times were also tracked

## Slide 22: Matrix Controller
Now with hardware to allow for external data input, a state machine controller is needed to complete computation
The controller needs to:
  Read data in the input buffer
  Pipeline data into the matrix accelerator
  Use matrix accelerator control signals to generate convolution sum
The controller has three main states:
  Reading data from the buffer
  Multiplying the input values
  Add the resulting products

## Slide 23: Convolution Accelerator Top Wrapper
A top-level package was created to wrap the input buffer, matrix accelerator, and controller into one design
Convolution Accelerator block diagram
This device has three dynamic configurations: Integer, Floating Point, Fixed Point

## Slide 24: Convolution Accelerator Top Wrapper (cont.)
This package is currently being prototyped and fails the implementation phase due to timing issues
Timing issues are generally caused by unstable signals or undesirable combinational logic delay

## Slide 25: Dynamic Resources
Floating Point Resources:

## Slide 26: Dynamic Resources
Fixed Point Resources:

## Slide 27: Dynamic Resources
Integer Resources:

## Slide 28: Conclusions
While much of the development process for RTL has streamlined by Xilinx, many times development and debugging could be quite strenuous
  Much of the development process is very well documented for users of Tcl but nothing else
    This often led to scrolling through forum posting for information rather than being able to rely on the official documentation
The Convolution Accelerator design needs to be refined
  Due to the mentioned timing issues, the design would not function properly on the Pynq-Z2
  The floating-point adder uses much more resources than any other device in the project

## Slide 29: Thank You