## Slide 1
Convolution Processing Unit
Featuring Adaptive Precision using Dynamic Reconfiguration
David Cain, Omar Eldash, Kasem Khalil, Magdy Bayoumi
WF-IoT 2021 Paper
Presented by David Cain

## Slide 2: Overview
Introduction
  Computer Vision
  Traditional IoT CNN Models
  Hardware Accelerator Types
  Reconfigurable Hardware
  Dynamic Partial Reconfiguration
Related Work
Proposed Convolution Processing Element
Hardware Implementation & Comparisons
Conclusions
Q&A
1

## Slide 3
2
Computer Vision
Computer vision is a field which aims to develop models for computers to understand and interpret image data
Unique edge devices with image and video data are being created for these applications in mind
The CNNs used are often complex and too computationally bulky for IoT edge devices

## Slide 4
3
With traditional cloud computing models, edge devices are “dumb” data aggregators
- Zombie device
Cloud servers perform CNN processes
Dedicated server hardware has much greater processing capabilities and relaxed power constraints compared to edge devices
High connectivity required…
How to get these processes local to the edge device?
Traditional IoT CNN Models

## Slide 5
4
Hardware Accelerator Types
– ex. nvidia Jetson Nano
– NVIDIA JetPack SDK, TensorFlow, PyTorch
– ex. Xilinx Virtex UltraScale+
– Verilog, VHDL, HDL
– Verilog, VHDL, HDL
– ex. Intel’s Movidius Myriad X
– Propriety Intel MDK
Graphics Processing Unit
(GPU)
Vision Processing Unit
(VPU)
Application-Specific Integrated Circuit
(ASIC)
Field Programmable Gate Array
(FPGA)

## Slide 6
5
Here, FPGAs are being investigated for hardware accelerating the CNN process at the edge devices
Low development overhead
FPGAs are classified as reconfigurable hardware by changing behavior or functionality at the hardware logic level
FPGAs offer Dynamic Partial Reconfiguration (DPR)
Reconfigurable Hardware

## Slide 7
6
DPR allows the device to partially reconfigure while the rest of the system remains unchanged
Offline Reconfiguration
Online Reconfiguration
Modern DPR design flows use reconfigurable regions with partition definitions to be loaded after full configuration
DPR can minimize system downtime as only individual blocks of the design can be updated
Dynamic Partial Reconfiguration

## Slide 8
7
Related Work
Deploying CNN Models on FPGA
Ref: Christos Bouganis, “Tool-flows for mapping CNNs into FPGAs: Trends and Challenges”
FINN is developed by a Xilinx research group and specializes in low latency architectures
- Streaming Architecture
- Modeled with HLS
FINN Ref: https://xilinx.github.io/finn/about.html
DNNWeaver is an open-source framework that employs groups universal processing elements and a state machine to assign data to one layer of the CNN at a time
- Single Computation Engine
- Modeled with Caffe
DNNWeaver Reg: http://dnnweaver.org/

## Slide 9
8
Related Work
Youssef et. al developed an MNIST CNN architecture to support DPR for reducing bit precision which enables lower dynamic power consumption
The energy consumption of this model at 16 bits was shown to be 11.25μJ per image and at 5 bits, 3.02 μJ per image while retaining 81.74% accuracy
Using DPR for configuring the full CNN pipeline with DPR
Ref: E. Youssef, H. A. Elsemary, M. A. El-Moursy, A. Khattab and H. Mostafa, "Energy Adaptive Convolution Neural Network Using Dynamic Partial Reconfiguration," 2020 IEEE 63rd International Midwest Symposium on Circuits and Systems (MWSCAS), Springfield, MA, USA, 2020, pp. 325-328, doi: 10.1109/MWSCAS48704.2020.9184640.
Energy Adaptive CNN using DPR
DPR Input Trigger
Reconfigurable Region

## Slide 10
9
Related Work
Rupani et. al present a convolution processing model which utilizes parallel data paths for handling flexible requirements of CNN
This means when one filter is selected, remaining hardware is idle and unavailable for use
Ref: Rupani, Ajay & Whig, Pawan & Sujediya, Gajendra & Vyas, Piyush. “Hardware Implementation of IoT-Based Image Processing Filters,” (2018).
Convolution Processor Using Parallel Pipeline

## Slide 11: Proposed Convolution Processing Element
Introduction
  Computer Vision
  Traditional IoT CNN Models
  Hardware Accelerator Types
  Reconfigurable Hardware
  Dynamic Partial Reconfiguration
Related Work
Proposed Convolution Processing Element
Hardware Implementation & Comparisons
Conclusions
Q&A
10

## Slide 12
11
Proposed Convolution Processing Element
CPE features a convolution controller, line buffers, and matrix accelerator

## Slide 13
12
Proposed Convolution Processing Element
Hard Synth Parameters
(Not partially reconfigurable):
- Process Channel Count
Kernel Size
Hardware Reconfig Parameters:
Data Precision
Only convolution layer of CNN is implemented/evaluated
The proposed Convolution Processing Element utilizes DPR at a processing element level
Traditional FPGA methods must either fully reconfigure, implement parallel data paths, or use DPR at a pipeline level

## Slide 14
13
Proposed Convolution Processing Element
The convolution controller handles the data stream with an internal state machine
For a kernel of size N, the line buffers temporarily store N rows of input map as each convolution requires NxN data points from N rows and N columns
Line buffers are implemented to infer into BRAM as to not waste available device logic

## Slide 15: Hardware Implementation & Comparisons
Introduction
  Computer Vision
  Traditional IoT CNN Models
  Hardware Accelerator Types
  Reconfigurable Hardware
  Dynamic Partial Reconfiguration
Related Work
Proposed Convolution Processing Element
Hardware Implementation & Comparisons
Conclusions
Q&A
14

## Slide 16
15
Hardware Implementation & Comparisons
Implemented on a Pynq-Z2 which features a Zynq-7000 FPGA
Reconfigurable between 8-, 16-, and 32-bit precision with 1 or 3 processing channels
Benchmarked using PYNQ Python Jupyter Notebook and the Vitis C environment

## Slide 17
16
FPGA has several ways to programmed on boot that vary with device family
The Zynq device used in implementation allows programming over Serial, JTAG, ICAP, and PCAP
The port bandwidth varies drastically
Dynamic Partial Reconfiguration
Ref: Xilinx UG585 Zynq-7000 SoC Technical Reference Manual
Ref: Xilinx UG909 (v2018.1) Partial Reconfiguration

## Slide 18
17
Dynamic Partial Reconfiguration
Reconfigurable Regions
Reconfigurable regions are manually mapped to the FPGA floorplan during Synthesis
If the partition definitions need special elements like DSP, the region must be mapped to include this
3 channel convolution processor with RR mapped to FPGA floorplan

## Slide 19
18
Hardware Implementation & Comparisons
(Traditional)
Full Reconfiguration
Using JTAG
(Proposed Implementation)
Partial Reconfiguration at processing element level
Using ICAP
Bitstream Size:
32,364,512 b
Port bandwidth:
66 Mb/s
Reconfiguration Time:
490.371 ms
Bitstream Size:
1,766,976 b
Port bandwidth:
3.2 Gb/s
Reconfiguration Time:
0.552 ms
As traditional methods would reconfigure the full device via JTAG,
using DPR at a processing element level reduces configuration time by 800x

## Slide 20
19
Hardware Implementation & Comparisons
At the 32-bit configuration, DSP utilization reaches 36% of total available for the device
- This is a limited resource for larger systems so lower precisions should be considered
The proposed 3-channel CPE hardware utilization was compared against other designs
Rupani et. Al [16] use a design which buffers the full image which causes high BRAM utilization

## Slide 21
20
Hardware Implementation & Comparisons
When testing with Jupyter Notebooks (Left), reconfiguration was completed using JTAG
Benchmarking was moved to Vitis (Right) which enabled use of the ICAP for reconfiguration
System Operating Frequency: 100 MHz

## Slide 22: Contributions & Conclusions
The proposed design provides insight to a design flow which enables system downtime to be minimized if pipelines are strategically queued and reconfigured
The proposed design architecture can be elaborated further to reuse hardware for process parallelization at lower precision, etc.
With these contributions in mind, reconfigurable hardware enables resource efficient processors to be developed for application specific needs
Reconfigurable hardware offers Dynamic Partial Reconfiguration which greatly suits the computationally constrained hardware systems found in IoT embedded devices

## Slide 23: Thank You

## Slide 24: Questions?